## Slide 1: Recommendations for upcoming 1800 PAR
SV-DC

## Slide 2: Introduction
user-defined nettypes (UDNs) & interconnect were added in P1800-2012
  The features were intentionally very restrictive
  Usage would determine how to relax the restrictions
    Users have enough experience to make requests
  Important features were missing due to time constraints
SystemVerilog/Verilog-AMS effort has started
  SV-only features needed for the SV/VAMS effort should come into SV through SV-DC
SV-DC needs to develop several major enhancements to meet user needs
  Work items have been categorized into MUST, SHOULD, and COULD in SV-DC Roadmap document

## Slide 3: MUST items
UDN/interconnect usability issues
  R01: Variable connections to UDNs and interconnect
  R03: Heterogeneous concatenations involving UDNs and interconnect
R02: Switch primitives that support UDNs
R05: Adapters (i.e., conversion elements) between non-matching UDNs
  Rules for selecting and specializing adapters
  Scheduling of adapter evaluation in the simulation cycle
  UPF/multiple power supply support

## Slide 4: SHOULD items
R04: Partial drive of UDN struct fields
R06: Allow sensitivity to UDNs/aggregates in even controls
  Recommended that SV-BC take up this item
  SV-DC will provide requirements on the UDN side
R07: Access to the name of drivers (elements in the resolution function input array) and the resolved net within a resolution function
  VPI is a good solution here
  Recommended that SV-CC add a data model for nettypes in VPI
R08: Limited read/write access to external variables from within a resolution function
R10: Late binding of resolution functions
R11: Access to the state of the resolved net inside a resolution function

## Slide 5: COULD items
R09: Advanced runtime timing control
R12: Ability to keep state in a resolution function

## Slide 6: Recommendation & rough plan
To accomplish the MUST items SV-DC requests 2 years of TC working time
  Rough expectation is that R01 and R03 can be handled while SV-DC waits on a recommendation for R05 from SV/VAMS
    Goal is to have a first draft recommendation for R05 from SV/VAMS by early fall 2015
  R02 can proceed in parallel
  SHOULD items can be interleaved as needed

## Slide 7: Additional resources
SV-DC Roadmap: http://goo.gl/OOI0gN