## Slide 1: VHDL-200x DAC 2003 Birds of a Feather
VHDL-200x Steering Committee Members
IEEE
VHDL-200x
Stephen Bailey, VASG Chair John Willis, ISAC and Fast-Track Jim Lewis, Modelling & Productivity J. Bhasker, Testbench & Verification
John Ries, Performance Rob Anderson, Assertions Paul Menchini, Data Types & Abstraction Joshua Johnson, Asynchronous Design

## Slide 2: Agenda
IEEE information
What is VHDL 200x?
What is the Schedule?
How does VHPI fit in?
What is the organization?
Enhancements (by functional team)
Contact information

## Slide 3: Instructions for the WG Chair
At Each Meeting, the Working Group Chair shall:
Show slides #1 and #2 of this presentation
Advise the WG membership that:
  The IEEE’s Patent Policy is consistent with the ANSI patent policy and is described in Clause 6 of the IEEE SA Standards Board Bylaws;
  Early disclosure of patents which may be essential for the use of standards under development is encouraged;
  Disclosures made of such patents may not be exhaustive of all patents that may be essential for the use of standards under development, and that neither the IEEE, the WG nor the WG Chairman ensure the accuracy or completeness of any disclosure or whether any disclosure is of a patent that in fact may be essential for the use of standards under development.
Instruct the WG Secretary to record in the minutes of the relevant WG meeting:
  that the foregoing advice was provided and the two slides were shown;
  that an opportunity was provided for WG members to identify or disclose patents that the WG member believes may be essential for the use of that standard;
  any responses that were given, specifically the patents and patent applications that were identified (if any) and by whom.
(Not necessary to be shown)
Approved by IEEE-SA Standards Board – December 2002
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: IEEE-SA Standards Board Bylaws on Patents in Standards
  6. Patents
  IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard. This assurance shall be provided without coercion and prior to approval of the standard (or reaffirmation when a patent becomes known after initial approval of the standard). This assurance shall be a letter that is in the form of either
  a) A general disclaimer to the effect that the patentee will not enforce any of its present or future patent(s) whose use would be required to implement the proposed IEEE standard against any person or entity using the patent(s) to comply with the standard or
  b) A statement that a license will be made available without compensation or under reasonable rates, with reasonable terms and conditions that are demonstrably free of any unfair discrimination
  This assurance shall apply, at a minimum, from the date of the standard's approval to the date of the standard's withdrawal and is irrevocable during that period.
Approved by IEEE-SA Standards Board – December 2002
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Inappropriate Topics for IEEE WG Meetings
Don’t discuss licensing terms or conditions
Don’t discuss product pricing, territorial restrictions or market share
Don’t discuss ongoing litigation or threatened litigation
Don’t be silent if inappropriate topics are discussed… do formally object.
If you have questions,
contact the IEEE Patent Committee Administrator
at patcom@ieee.org
Slide #2
Approved by IEEE-SA Standards Board – December 2002
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: What is VHDL-200x?
The next language revision (or two)
Significant enhancements are planned
  Not another “bug-fix release”
Focus is on:
  Performance & productivity
  Testbench & verification
    Assertion-based verification (ABV)
  Modeling

## Slide 7: Schedule
Fast-Track
DAC ‘03
Dec ‘03
Dec ‘04
1st Ballot
Final list
VHPI
LRM Edit
1st Ballot
DAC ‘04
VHDL-200x (1)
LRM Edit
1st Ballot
VHDL-200x (2)*
LRM Edit
DAC 05
*If needed

## Slide 8: Where are We Today
Organized into teams
Prioritized enhancement requests
Some teams have published proposed language changes
Others have started some analysis of requirements
Others have not yet made significant progress
  Post DAC it is important that they do begin making progress

## Slide 9: How Does VHPI Fit In?
VHPI LRM editing is funded
  Thanks Accellera!
FT and VHPI both ready to ballot in Dec?
  Ballot 2 PARs individually
  Ballot 2 PARs together
  Fold into 1 PAR and ballot together
  Recommendation: Fold into 1 PAR
    Ensure FT & VHPI changes integrated

## Slide 10: VHDL 200x Organization
Fast-track
Modeling & Productivity
Performance
Assertions
Testbench & Verification
Data Types & Abstraction
Environment
Asynchronous Modeling

## Slide 11: Enhancements by Functional Team

## Slide 12: Top Priorities
Direct C & Verilog calls / std I/F
Text IO
to_string type capabilities
Reading of out mode ports
Performance
Assertions
  Apply Accellera assertions (PSL)
Some modeling enhancements
Environment (simulaton control routines)
Generate enhancements
Testbench / verification
Object-oriented enhancements

## Slide 13: VHDL 200x Fast Track
John Willis and Jim Lewis vhdl-200x-ft@vhdl.org http://www.vhdl.org/vhdl-200x/vhdl-200x-ft

## Slide 14: VHDL-200x-FT Charter
Make critical updates to the language to support other standards groups (such as IEEE P1164, IEEE P1076.3, and Assertions).
Select additional enhancements that:
  Have low LRM impact
  Non-controversial
  Relatively high benefit

## Slide 15: VHDL-200x-FT Requests
Issue
Allow explicit operators (ie: ">") to overload implicit operators
Unary Reduction Operators (and, or, xor, ...). Also see 1164 & numeric_std.
Array/scalar logic operations
Min/max operations for types with defined "<" and ">" operations
to_string, to_hstring, to_ostring
'image (for all types)
Index
FT1
FT2
FT3
FT4
FT5
FT6
Status
Analyzed by ISAC
Analyzed by 1164
Analyzed by 1164
Proposed
Proposed
Proposed

## Slide 16: VHDL-200x-FT Requests
Issue
Standard Signal Spy / XMR capability (package/procedural based)
hwrite, owrite, dwrite, bwrite, hread, oread, dread, bread
Index
FT7*
FT8
Status
Proposed
Analyzed by 1164
* Status of FT7
Have donation from MTI. Expecting donation from Cadence. Are in early stages of discussion with Synopsys.

## Slide 17: VHDL-200x-FT Status
Leverage off of work being done by the 1164 and 1076.3 working groups.
We are actively looking for champions for proposals

## Slide 18: VHDL 200x Modeling and Productivity
Jim Lewis vhdl-200x-mp@vhdl.org http://www.vhdl.org/vhdl-200x/vhdl-200x-mp

## Slide 19: VHDL-200x-MP Charter
Improve designer productivity through enhancing conciseness, simplifying common occurrences of code, and improving capture of intent.
Enhance VHDL to allow (easy) modeling of functionality which is currently difficult or impossible.

## Slide 20: VHDL-200x-MP Requests
General Proposals
Bidirectional Connections (Switch, Jumper, Resistor)
Regularized and minimized bracketing (end)
Allow concurrent assignments (conditional and selected) in sequential code
Create a one dimensional array aggregate. Permit it to be used on LHS of assignment
*Permit expressions to be mapped to signal ports of entities and subprograms.
More locally static expressions. Things like concatenation, indexing, and slicing of static objects/values
Allow attribute declarations in code regions (not just decl)
* Candidate for Fast Track (Simplifies use of OVL)

## Slide 21: VHDL-200x-MP Requests
Entity
Allow ";" to terminate as well as separate an interface list
Eliminate passive statement restriction on entities
Package
Allow subprogram bodies in package declaration region

## Slide 22: VHDL-200x-MP Requests
Types, Operators, and Overloading
Give bit_vector an unsigned interpretation.
Create rising_edge and falling_edge for type bit.
Integrate 1164, 1076.2, 1076.3 into 1076
Create comparision operators that return std_ulogic. ?EQ, NE, GT, LT, GE, LE?
Boolean equivalence (of sl and boolean). if sl then
Ability to apply register kind semantics to std_logic. Retain last resolved value when all drivers are off.
* Max function (also listed in fast track)
Remove white space requirement in physical literals.
Short alias name for std_logic_vector.
Value folding of std_ulogic (2 state/4 state).

## Slide 23: VHDL-200x-MP Requests
Generate
Add else/elsif clause in if-generate
Case generate.
Components and Instantiations
Implicit generic/port map in component instance
Process
Permit keyword "all" or alternately symbol "*" in sensitivity list to imply all signals read in the process are in the sensitivity list
Loop
Longest static prefix issue with loops

## Slide 24: VHDL-200x-MP Requests
If Statements
Add Endif (like elsif). See also general stuff about regularizing syntax and end
Orif, orels, etc for mutual exclusive branches in FSM
Case Statements
Case Statement expressions (index & choices)
Don't cares in case statement targets and comparison operators
Non-locally static expressions in case expressions.

## Slide 25: VHDL-200x-MP Status
We are actively looking for proposals
We are actively looking for champions for proposals

## Slide 26: VHDL-200x Performance
Chairman: John Ries johnr@model.com E-mail: vhdl-200x-perf@eda.org
http://www.eda.org/vhdl-200x/vhdl-200x-pref

## Slide 27: Scope and Responsibilities
Language changes that increase the speed of tools.
Mostly focused on simulator performance.

## Slide 28: Performance Proposals
Zero-delay ordering of signals
Removal of simulation deltas
Define 2 & 4 state semantics
Atomic composite signals
Expressions in sensitivity lists

## Slide 29: Performance Proposals(2)
Sensitivity to all signals read
Light-weight signals
Architecture level signal drivers
Removal of deprecated constructs

## Slide 30: VHDL-200x Assertions
Chairman: Rob Anderson rob@reawebtech.com E-mail: vhdl-200x-asr@eda.org
http://www.eda.org/vhdl-200x/vhdl-200x-asr

## Slide 31: Scope and Responsibilities
Enhance VHDL to provide support for Assertion-Based Verification
  Primarily this means adding support for temporal expressions/sequences with assertions
  Secondarily also includes API for coverage data
  Want to leverage work of PSL and SystemVerilog assertions

## Slide 32: Current Status
Currently analyzing and comparing the capabilities of PSL and SystemVerilog Assertions
Next step: determine if anything is missing
  Especially from a VHDL perspective
Expect PSL or SVA adoption as initial draft
  How much deviation or enhancement TBD

## Slide 33: Assertions Schedule
Finish PSL / SVA comparison in June
Publish comparison
Determine & publish any additions desired for VHDL by mid July
Determine VHDL starting point by Sep
Finish technical proposal by Mar ‘04

## Slide 34: VHDL-200x Testbench & Verification
Chairman: J. Bhasker jbhasker@esilicon.com E-mail: vhdl-200x-tbv@eda.org
http://www.eda.org/vhdl-200x/vhdl-200x-tbv

## Slide 35: 1076-200x: TBV Group
Testbench and verification group
List of issues under consideration posted on our home page – For eg. sparse arrays, constrained random number generation, lists, events.
A couple of proposals on the table
WG is active - started teleconferences
Associative arrays and fork-join features discussed
http://www.eda.org/vhdl-200x/vhdl-200x-tbv
Questions? Jbhasker@esilicon.com

## Slide 36: Associative arrays
-- Type declarations:
type myaaT is associative (INTEGER) of BIT;
type COLOR is {Red, Blue, Green, Yellow, Orange};
type my2aaT is associative (COLOR, COLOR) of INTEGER;
-- Two associative arrays:
variable mem_aa: myaaT:
signal matrix: my2aaT;
-- Implicit subprograms:
Delete, exists, size, first, last, next, prev

## Slide 37: Fork & Join
<fj_label>: fork -- Sequential statement
<seq_blk1>: declare -- Sequential block; allowed outside
-- of a fork-join context as well.
<local_declarations>
begin
<sequential_statements>
end declare <seq_blk1>;
<seq_blk2>: declare
<local_declarations>
begin
<sequential_statements>
end declare <seq_blk2>;
join all <fj_label>; -- none / first / condition_clause/
-- timeout_clause

## Slide 38: VHDL 200x Data Types and Abstraction
Paul Menchini
vhdl-200x-dta@vhdl.org http://www.vhdl.org/vhdl-200x/vhdl-200x-dta

## Slide 39: VHDL-200x-dta Charter
Enhance VHDL data types abstractions.
Serve as a resource to other groups contemplating changes to the existing VHDL data types and abstraction mechanisms.

## Slide 40: VHDL-200x-dta Responsibilities
Collect suggestions for change
Analyze suggestions for change
Analyze proposals and language designs from other subgroups
Develop language designs for changes and proposals
Recommend changes to language in dta

## Slide 41: VHDL-200x-dta Requests
Object Oriented Features
Variant Records (“free unions”)
New standard data types
  Boolean, integer, real vectors
Associative arrays
Sparse arrays
Enhanced object initialization
Built-in lists

## Slide 42: VHDL-200x-dta Status
We wish to leverage off of previous work (e.g., in OO and variant records)
We are actively looking for proposals
We are actively looking for champions for proposals

## Slide 43: VHDL 200x Environment
Dennis Soderberg
vhdl-200x-env@vhdl.org
http://www.vhdl.org/vhdl-200x/vhdl-200x-env
IEEE
VHDL-200x

## Slide 44: VHDL-200x-Env Charter
Standardize handling of non-VHDL constructs.
Enhance platform interoperability

## Slide 45: VHDL-200x-Env Requests
General Proposals
Add simulation control environment
Simulation control subprograms
Environment
External Interface

## Slide 46: VHDL-200x-Env Status
We are looking for more proposals

## Slide 47: Additional VHDL Enhancement Standardization Projects

## Slide 48: VHPI standard Status John Shields, Françoise Martinolle
Notes: Sound check
On behalf of the committee, we appreciate the opportunity to talk to you about VHPI today. I will define it and motivate its value, comment on our approach, briefly illustrate its main features, and finally say where we are and what is left
to do.

## Slide 49: VHPI Technical status
Technical specification is done
  It covers: post-analysis, elaboration and runtime VHPI access
Final draft is available on web site http://www.vhdl.org/vhdlpli
Editorial work
  Initial funding (20%) provided by Accellera
  Paul Menchini has begun incorporating VHPI in the VHDL 1076 LRM
  First funded phase supposed to end June 15 (on track)
    Integrate VHPI significant control points into elaboration and simulation.
    Define common terminology
    Organize and outline the additional chapter(s) and appendices of the VHDL LRM

## Slide 50: VHDL 1076 deliverables
VHPI integrated in the VHDL LRM 1076
A CD containing the formal XML representation of the VHPI static and dynamic information model (binary readable)
  Today the IEEE allows provision of a companion CD

## Slide 51: Working Group status
The WG is:
  closing any remaining open issue
  interacting with and reviewing Paul’s first draft
  organizing in parallel a comprehensive review of the current VHPI specification

## Slide 52: Road map
Goal is to have a ballotable LRM by end of October and go to ballot by 2003 end.
Started to:
  incorporate critical sections affecting VHDL semantics first
  identify experts to early review draft versions

## Slide 53: VHPI industry implementations
Many companies have already provided some level of VHPI implementation to customers
      Vendors include: Cadence, Synopsys, FTL systems…
      Tools already using VHPI: Debussy, Verisity, Vera…
Key vendors projected to aim at compliance by DAC 2004

## Slide 54: 1076.6 VHDL Synthesizable Subset
Chair: J. Bhasker jbhasker@esilicon.com

## Slide 55: 1076.6
Standard for VHDL RTL Synthesis
First standard out in 1999 (IEEE Std1076.6-1999)
WG diligently worked on next rev for past couple of years
Next revision draft is ready for ballot
Revision PAR just approved by IEEE
Ballot and standardization expected by EOY
http://www.eda.org/siwg, siwg@eda.org

## Slide 56: P1164 Status
Peter Ashenden Ashenden Designs
P1164 Chair
peter@ashenden.com.au
vhdl-std-logic@eda.org
www.eda.org/vhdl-std-logic
IEEE
VHDL-200x

## Slide 57: Standard Revision
Changes to enhance usability
Adding functions and operators
Adding textio support
No major conceptual changes
To be balloted by end-2003
www.eda.org/vhdl-std-logic

## Slide 58: Accepted Changes To Date
Uncomment "xnor" operators
Shift operators for vector types
Vector/scalar logic operators
  scalar is replicated to vector’s length
Logical reduction functions
Match functions

## Slide 59: Rejected/Pending Changes
Rejected
  Subtype of vector results
  Capacitive strength (deferred)
  'image (refer to VASG)
Pending
  std_logic_textio package (donated by Synopsys)
  to_string functions

## Slide 60: Articulation with VASG
Vector/scalar operators for bit_vector
Logical reduction functions for bit_vector
  or unary logical reduction operators
Generalize 'image to composite types
Radix-formatted textio
To_string functions