## Slide 1: P1735 Standard Overview
Based on Draft 3 and 3a work in progress
John Shields
Mentor Graphics, Inc.

## Slide 2: Agenda
IEEE protection
P1735 Goals
P1735 V1 Recommendations
P1735 V2 Recommendations
P1735 Status and Plan
Impact on 1800, 1076, other IP representations
P1735 Future
*Out of Scope for Today*

## Slide 3: Out Of Scope For Today
Tutorial on conceptual model for IP protection
Security risks
Status of industry tool support
How to build IEEE protection into HDL-based tools
Notes: Not saying these are not interesting or that some of the audience might want to talk about them!
Not promising to do this at a future date either!

## Slide 4: IEEE Protection
Pragmas defined in SV and VHDL LRMs
Describes encryption and decryption envelopes
Promise of interoperability
Policy free, forward looking markup of HDL representation of IP

## Slide 5: IEEE Protection – Historical Reality
LRMs difficult to understand
Intentional uncertainty to avoid export law conflicts
Use case and some details not adequately defined for interoperability
Early implementations only worked within vendor specific tool flows
Stakeholders had a shopping list of enhancements
Notes: Historical because things are better today because of P1735 efforts

## Slide 6: What is P1735?
IEEE P1735
  Recommended Practice standard
  Covers Encryption and Rights Management for Electronic Design IP
  Coordinating group for IP protection in IEEE Design Automation standards
P1735 Goals
  Achieve interoperability across heterogeneous tool chains
  Define better use models
  Add rights management mechanism for IP authors
  Improve pragmas to match intent
  Make IEEE protection more understandable to IP authors, IP users, and tool vendors
Notes: * you can read the PAR for P1735
* No expectation this would be achieved in 1 single step

## Slide 7: P1735 V1 Recommendations
Arose from industry effort to resolve issues with IEEE protection pragmas
  Mutual customers demanded a correct solution
  Existing implementations were technically correct, but wouldn’t work together
V1 achieved basic interoperability across tool flows
  Many vendors and tools have validated support today
Available* in 2 forms
  Early unpublished work in progress within the WG
  Part of the final draft of P1735
Its the de-facto standard today
Notes: * It is private to P1735 working group members only

## Slide 8: P1735 V1 Summary
Digital envelope use model
Inline public key pragma clarifications
Consensus on required support for specific encryption algorithms and encoding
New version pragma for backward compatibility
  allows tool specific implementations co-exist
  Allows pragmas and use models to evolve

## Slide 9: P1735 V2 Recommendations – First Look
Improved Key Management
  Support of X.509 certificates for public key exchange
New framework(set of pragmas) for rights management
  admits both common and tool specific rights
A licensing model for IP authors
  Mechanism to grant per user access to IP
  Secure protocol for tool interaction with external licensing proxy
  Expressed as a condition on a right
A small, conservative set of common rights
  Error handling, visibility, decryption
  Seamless transition from the default responsibility of all tools
Better IP specific visibility control

## Slide 10: Key Management
Use inline public key pragma (v1)
  trust model (web of trust or peer to peer exchange, tool vendor to IP author)
X.509 certificates (v2)
  Additional defined trust model (CAs) possible
  Mapped to pragma schema
Encryption Tool Improvements possible
  Key database and utilities
Notes: People make a big deal of establishing trust for public keys in general, but public keys for a vendor tool can be validated by licensed users of the tool
Spoofing public keys may be possible in the key distribution, but spoofing the actual tool that the public key enables to work with IP is very high bar!
Key mgmt value is its separation from HDL code and the ability to leverage key vaults to manage a set of keys. It will matter in the future for IP author digital signing of IP and trust in the public key of the author

## Slide 11: Rights Management Framework
Rights block
  Plain text expression of rights for one or all tools
  Tamper proof construction
Basic rights syntax (simplified):
  `protect …,rights_block
  `protect control <right>=<value>
  `protect control <right>=<value> [, <condition>, <condition>, …]
  `protect …, rights_digest
  encoded encrypted rights block digest
Reasonable composition rules for multiple declaration of the same right
  with different conditions
  in common and tool-specific blocks

## Slide 12: Licensing
The ability to grant a right based on the availability of a license
  Per user control over what can be done with an IP
The licensing system contains the following components.
—License proxy is an executable provided by the IP author. It securely communicates with the EDA tool through a socket.
—License specification is several lines in a rights block, identifying the proxy, attributes, and a public key where the matching private key is hidden in the license proxy.
—License use is either a conditional rights assignment or an external right as described in Clause 7.
—Proxy communication is the details of secure message construction and communication between the license proxy and the EDA tool.
Notes: * This could be expanded beyond this overview and that will be valuable for some audiences

## Slide 13: Common Rights
Means the same thing to all tools
Default and delegated value of a right required
  default - semantics when a common right is not specified
  delegated – protect information but allow tool to operate for its intended purpose
Common conditions
  toolphase = compile | elaborate | run
  activity = simulation | synthesis | analysis | layout
  license
Common rights (legal conditions not shown)
  error_handling = delegated | nonames | srcrefs | plaintext
  runtime_visibility = delegated | interface_names | all_names
  decryption = delegated | true | false
Notes: * These are talking points and need more depth in the presentation material

## Slide 14: Visibility Management
Existing semantics are clarified
  Default expectation for all tools is a foundation
  …but it’s not enough
Existing visibility controls limitations are explained
  Encryption envelopes and viewport pragma
  Awkward, ill-defined, not portable
Model fidelity trumps blind protection
  It is invalid for a tool to modify the behavior of the model that the IP author wrote.
Toolphases have basic visibility requirements
  Compile and elaborate see everything
  Nothing is required to be made visible externally
Viewport pragma selectively exposes IP internals at runtime
Common rights for error handling and general use cases

## Slide 15: Boundaries Of First P1735 Standard
Visibility is still a complex area with open issues
  Representation specific visibility control can’t be addressed in P1735
  P1735 intends to offer some guidance and principles
Granularity of Encryption envelopes
  Design unit granularity recommended for interoperability
Relationship between disjoint protected envelopes
  None!
PLI
  Large language centric analysis of information models
Use of Obfuscation
  Orthogonal external mechanism that has value
  Other uses possible
Notes: * The overview isn’t complete without saying what isn’t addressed

## Slide 16: Tasks/Schedule Considerations for P1735
Internal WG draft comment period closes April 12th
D4 of draft in progress - inputs close April 15th
  Approval to ballot or revise further – April 29th
D5 is possible
Ballot group formation
  Goal is end of April
  We may postpone until after DAC
IEEE ballot in July
Sensitive to due process and financial constraints
  Revision/Reballot due to negative ballot feedback
  IEEE Revcom approval – august or december meetings
  Technical editor funding – must be done with D5 by May
  PAR expiration

## Slide 17: P1735 Impact on 1800, P1076, and others
Assuming acceptance, DASC assumes content revision to other standards implied
Scope of Update belongs to you
  We were guided not to refactor the specification of encryption
  Options
    Incorporate some material by reference
    Codify other aspects into LRM
  Petition DASC to charter new PAR to refactor LRM and P1735 for future revision
Some hard problems are still yours!
  See earlier slides
  They are intrinsically part of these standards, not P1735

## Slide 18: P1735 Future
Foster education, outreach, promotion activity
Study the need and timing of a follow-on PAR
  Potential Considerations
    refactoring - define a generic, complete pragma set with bindings to VHDL, SV, and potentially other representations
    focus on encapsulation of IP representations
    improve common rights
    Address unique considerations in other tool flow components
    Key management enhancements
    Improving IP protection security – best practices for piracy prevention
    Traceability – tagging and watermarking
The Working Group serves at the pleasure of the DASC under IEEE rules
  These comments about our future are our own expectations

## Slide 20: Scope of P1735
This standard specifies embeddable and encapsulating markup syntaxes for design IP encryption and rights management, together with recommendations for integration with design specification formats described in other standards. It also recommends use models for interoperable tool and hardware flows, which will include selecting encryption and encoding algorithms and encryption key management. The recommendation includes a description of the trust model assumed in the recommended use models. This standard does not specifically include any consideration of digitally encoded entertainment media. In the context of this document, the term IP will be used to mean Electronic Design Intellectual Property data.

## Slide 21: Electronic Design Intellectual Property
Electronic Design Intellectual Property is a term used in the electronic design community. It refers to a reusable collection of design specifications which represent the behavior, properties, and/or representation of the design in various media. Examples of these collections include, but are not limited to:
  A unit of electronic system design
  A design verification and analysis scheme (e.g., test bench)
  A netlist indicating elements and the interconnection thereof to implement a function
  A set of fabrication instructions
  A physical layout design or chip layout
  A design intent specification
The term is partially derived from the common practice for the collection to be considered the intellectual property of one party. Hardware and software descriptions are encompassed by this term.

## Slide 22: Background Material - PAR
Purpose of Proposed Standard: The intent of this document is to enable design flows that provide interoperability between IP sources, tools, integrators, and users of the IP. There is currently no defined, independent standard for describing IP encryption markup for design information formats. Each design format which incorporates IP encryption describes their markup differently leading to confusing interpretation. Users of those standards also lack a recommended practice for inter-operable use of IP encryption.

## Slide 23: Con’t
This document provides guidelines and recommended practice for use of IP protection markup syntax and key management to enable interoperable tool flows with IP and tools from a wide array of suppliers. It includes algorithm selection for encryption and encoding. This document specifies a generic set of embeddable markup syntax suitable for IP protection and rights management of arbitrary text files. These files represent potential inputs and outputs of EDA tools that would otherwise expose IP. The generic syntax of these directives may be suitably modified for a particular file format if there are syntactic conflicts and variations may be described in recommended practices.